## Slide 1
Introduction
Our project introduces a cutting-edge Face Recognition System utilizing the ESP32 Camera, designed to offer a seamless, efficient, and cost-effective solution for various applications, ranging from smart homes to secure workplaces.
The ESP32 is a low-cost, low-power system on a chip (SoC) with integrated Wi-Fi and Bluetooth capabilities, thus the project considers its hardware limitations.
The project also respond to the danger of spoofing, where unauthorized individuals may deceive the system using fake images or videos.
Main Goal
Develop a facial recognition system for door access utilizing ESP32-CAM module.
Create an anti-spoofing algorithm, all implemented on the ESP32-CAM.
Design a portable system that is not restricted to a specific network or a predefined list of authorized personal
A small component with low computational capabilities.
Severe memory constraints.
Challenges
Main Solution
Results
ESP32-cam door control system
Yael Tzadik & Eden Ishay, supervised by Johanan Erez
Face Detection
The system integrates three components:
ESP32-camera
External server using the HTTP protocol
External repository on an SD card
Communication between the device and the server is done via Wi-Fi.
Connection to WI-FI is done Via Bluetooth.
Authorized personal are loaded from SD card and can be changed by switching cards.
https://visl.technion.ac.il/projects/2024s08/ Technion, Haifa, July. 2024
Horizontal change
Smile Detector
Normalize the distances of the points using fixed nose points as reference (blue),
Detect:
20% increase in horizontal distance (red)
100% increase in vertical distance (green)
vertical change
Normalization reference
Face Recognition
MTMN model for face and landmarks detection
Media Pipe FaceMesh provides 468 landmark points.
We selected 20 anatomically optimal points to differentiate between individuals
MTMN architecture
Solution structure
ESP32-CAMERA component
The example code in the Arduino IDE crashes after recognizing more than 3 out of 5 people. Our system significantly improves this limitation.
Our system offers a more reliable solution with significantly fewer false positives.
Results – comparison with existing solution
Bluetooth connection
When starting the system or restarting it, a Bluetooth connection named “Door Lock” is available. It makes the system user friendly and mobile.
The ESP32-CAM can be communicated through Bluetooth terminal by the following the stages below:
Set-Up Using Bluetooth connection
Bluetooth terminal using mobile app
The facial recognition algorithm, based on facial landmarks, measures the distances between each landmark and a reference point.
These measurements are then compared to a database of distances from other images.
Full FaceMesh
20 landmarks
The image is sent to the server via HTTP protocol I JPEG format.
To expedite the image transmission process, all areas except the face are painted gray (0x808080) before sending.
Face detected
Communication time is reduced by 65%.